## Slide 1: Meter Technician Calibration Procedures
2017 Meter Technician Training School
Steven Sievert
Manager, Quality Certification Services Inc.
Technical Director, National DHIA
Chair, ICAR Subcommittee for Recording and Sampling Devices

## Slide 2: Topics to Cover…
      Principles of Operation
      Calibration Procedures
      Troubleshooting
      Meter Center Design

## Slide 3: Some Terminology for Tru-Test Meters
Sleeve
Nozzle
Cover/Cap
Body & Flask Top
Lower Valve & Housing

## Slide 4: Principle of Meter Operation
Measuring a volume of liquid passing through at a controlled rate and then diverting a precise amount into a calibrated flask to obtain and estimate the total weight of the liquid
Volumetric Meters
Notes: Cover tip
Radii on sleeve
Inside surface of cover
Inlet tube - join to body
Nozzle
Flask top

## Slide 5: Important Facts
The Meter takes a representative proportion of the total milk flow
  Measuring pounds of milk
The subsample must represent the entire milking letdown
  For accurate components analysis
  This can be achieved either
    by mixing the collected milk – Pull-Out, Ezi-Test, Farmer, Econo-Valve
    by taking a small amount of the milk as it flows by during the emptying process – Auto Sampler

## Slide 6: Vacuum Drop
There are five main things which affect vacuum drop:
  The type and model of meter
  The air admission rate
  The flow rate (diameter and length)
  The length of extra tubing added to the system to connect the meters
  The mounting position of the meter - high or low
Notes: High line is not so variable as the Meter cannot be mounted in too many different ways I.e. in all cases the milk has to go up.
In low line the mounting can make a difference to the direction that the milk goes I.e. all down or with some up.

## Slide 7: Standard Flow Water Test
Requires Air Admission Inlet
  Hole from a #60 drill bit
  After the in-line water restrictor
  24”- 36” from the meter inlet
Water Restrictor has 1/8” Opening
Flow Rate = 8 lbs/minute (4:34)

## Slide 8: Standard Flow Water Test - Options
  Closed Jar-to-Jar System

## Slide 9: Standard Flow Water Test - Options
  Use of Standard Flow Wand from Waikato
  & Tru-Test Fast Flow Bucket

## Slide 10: Dual Meter Water Test
Same set up at Standard Flow Water Test
Second Meter can be connected in series
  24”- 36” hose from outlet of meter 1 to inlet of meter 2
  No second air admission inlet is needed
Flow Rate = 8 lbs/minute (4:34)

## Slide 11: Dual Meter Water Test

## Slide 12: Fast Flow Water Test
63” From Bottom of Pail (restrictor) to Top of Meter Flask
  Use a Pre-Cut Stick to Quickly Verify
  Use a Marker or Tape to Mark Off 63”
Water Needs a Straight Run to the Meter
Wide Bore Meters = 58-65 Seconds
Standard Bore Meters = 65-68 Seconds

## Slide 13: Fast Flow Water Test

## Slide 14: Getting Started
Inspect Meter
Mount Meter on Rig
Verify Correct Height
  Fast Flow = 63” to Top of Flask
  Hose is Straight as Possible
Verify Water Volume
  16 Liters / 16 kg / 35.3 lbs
Verify Vacuum Level - 15” hg

## Slide 15: Meter Installation
The Meter should be mounted within ±5 degrees of vertical
Take-offs - install Meters between the sensor & milk line to maintain vacuum for agitation and sampling
Air Bleed - must introduce air into the line, usually at the claw

## Slide 16: Clean Equipment
Meter Rig
  Are Hoses in Good Condition?
  Is Water Changed Regularly?
    Field Techs Are Supposed to Keep Meters Clean!
  Vacuum Pump Maintenance
    “If I adjust it, it could break”
    “What Oil????”

## Slide 17: While You Run
Check for:
  Air Leaks
  Blockages / Flow Restrictions
  Abnormal Performance
Remove Old Calibration Tag

## Slide 18: Meter Calibration Requirements
All meters must be calibrated at least once every 12 months
Calibrated to:
  2% accuracy on single weight
  3% accuracy on two consecutive weights
Data is reported to QCS as part of annual field service audit

## Slide 19: Meter Calibration Requirements

## Slide 20: Meter Calibration Tag Options
  Guidelines require tag with meter center name along with month and year of calibration

## Slide 21: Reporting Meter Calibration Results
Proper reporting improves audit efficiency
  Unique serial number – avoid alphanumeric values
  Make and model of meter
  Calibration date(s)
  Meter center and technician name
  Calibration weights
  Status during the audit period
Scale no | FT | Make | Model | 2013 Date | 2014 Date | Int | MC | MT | Initial | Second | Final | 2015 Status | 2016 Status
174434 | 999 | Tru-Test | WB AS | 7/7/2016 | 9/12/2016 | 67 | Meter Center Name | Meter Tech Name | 37.5 | 37.5 |  |  | RTS 2016

## Slide 22: Reporting Meter Calibration Results
Suggested Status Codes for Meter Calibration Worksheets
  Active
  New (+ year) – meter new from the box
  Return (+ year) – repaired meter or returned to active status
  Storage – calibrated meter not in active use (backup)
  Out (+ year) – meter taken out of service
  Perm Out or POS – broken meter (body) that cannot be repaired

## Slide 23: Periodic and Annual Maintenance
Milk meters should be periodically checked and maintained
  Disassemble and clean the sample valve and meter body. Info Sheets and brushes are available for this procedure.
  Wash all parts in very hot water with a proper dairy detergent.
  Rinse all parts in clean water after the hot detergent wash.
Notes: Have valves to disassemble

## Slide 24: Periodic and Annual Maintenance
Inspect all rubber parts for cracks and wear in order to minimize build up of bacteria “grunge” and to assure proper sealing of gaskets and O-rings.
Use a safety pin or “pick” to remove the o-rings so that the plastic grooves are not scratched or damaged.
Water test to ensure that the meter is in proper calibration.

## Slide 25: Several Runs Later….
If You Can’t Check the Water Before Each Run, Then……
  Now is a Good Time to Verify Water Level
How clean is the test water?
  You Know What to Do!!!
Is Vacuum Gauge Holding at 15” hg?

## Slide 26: Maintaining Water Volume
Electronic scale is best
Etch or tape a mark on the float pail or jar
If it is a float pail - is the float working?
  Float Should Move Freely
  Most Floats are in Disrepair

## Slide 27: Cleaning
Most dairy detergents can be used at the strengths recommended by the manufacturer
These chemicals attack polysulfone plastics that make up the key meter components
Avoid contact with:
  Direct Sunlight
  Petrochemicals & Hydrocarbons such as fly spray, brake or hydraulic fluid, WD40, lubricants, super glue, alcohols, and fuels
Notes: Turn valve to sample position while flask is full to empty through valve and wash it out.

## Slide 28: Trouble Shooting
Milk Meter Cover
Symptoms = abnormal readings
    Cap Point Sharp & Smooth
    Seated properly on Body
Look for Internal Scratches or Damage
Notes: Point - abrasions and dents
Scratches - especially Metering quadrant

## Slide 29: Trouble Shooting
Nozzles
    Gap across the nozzle is very controlled to ±0.01mm (0.0003”)
    Check for scratches or ridges on top
    Seated properly in holder
    Abrasion or signs of wear on sides
    Debris (cottonseed, corn, etc.)

## Slide 30: Trouble Shooting
Sleeve & Funnel
  Should be concentric - 3 legs seated properly - Not Loose
  No nicks or scratches since they will affect how the milk is spread out onto the inside of the cover
  Objects lodged inside or lower in the meter base – watch for broken baffle pieces lodged inside the rubber sleeve

## Slide 31: Trouble Shooting
Meter Body
  Look for possible leaks
    Symptoms = Low Reading or Hissing
      Check rubber flask seal – not rolled
      Look for hairline cracks
      Is the rocker free to pivot and seal?
  Look for possible blockages
    Symptoms = slow draining, no stirring

## Slide 32: Trouble Shooting
Cracks in Body or T-piece
  Generally caused by one of four factors
    Being dropped during loading/unloading
    Chemical or alcohol attack
    Improper disassembly or handling
    Hoses put on too far (3/4” is plenty)
    Parts that have been molded in or glued in during the assembly process are annealed to reduce the stresses

## Slide 33: Trouble Shooting
Milking Equipment Problems
  Areas to check:
    Air admission hole in claw must be open
    Adequate vacuum pump capacity/setting
    Condition of gaskets & O-rings - air leaks?
    Proper installation height of meters
    Length of hoses used to connect meters

## Slide 34: Worker Friendly Meter Center
Is Your workspace really a workspace?
  Dedicated work area for meter repairs
  Adequate lighting and ventilation
Arrange your area for efficiency
  Parts within reach
  Tools nearby and tools you need
  Workbench close to calibration rig and parts

## Slide 35: Clean Work Area Makes a Difference
Are you stepping over things?
  Floors clutter free?
  Meters stored to prevent damage?
Are things put away when you’re done?
Are you moving yesterday’s work out of the way so you can work today?
Are floors clean dry / non-slip?

## Slide 36: General Observations from Meter Centers
  Platform scales for initial water verification are failing
    Limited lifetime
    Usually one of four load cells fails leading to scale being off by a percentage
    Limited options under $200

## Slide 37: General Observations from Meter Centers
  Still observing unapproved meter modification in some affiliates
    Modification of parts so the meter samples faster resulting in inaccurate samples
    Removal of ball in valve of the Tru-Test Ezi-Test meter
    Cutting the tap of the Waikato MK V meter
    Modification of the sampler in the Tru-Test Auto Sampler meter

## Slide 38: General Observations from Meter Centers
  Equipment is aged beyond useful life in many meter centers
    Vacuum pumps/gauges are failing
      8 in 2014, 2 in 2015, 6 in 2016
    Receiver jars with air leaks, buildup
      5 in 2014, 5 in 2015, 7 in 2016

## Slide 39
    Trying to repair cracked bodies or caps with glues/cement
    Weakens the whole meter
    Introduces air leaks
    Not approved for Grade A dairies (PMO/FDA)
General Observations from Meter Centers

## Slide 40: General Observations from Meter Centers
  Unapproved meter modification
    Trying to repair broken hose nipples on bodies or caps
    Brass hose connectors
    Ballpoint pens
    Not approved for Grade A dairies (PMO/FDA)

## Slide 41: Keeping Flasks Looking Great
Remove cloudiness from aged flasks
Makes washing/cleanup easier
Notes: Turn valve to sample position while flask is full to empty through valve and wash it out.

## Slide 42: Keeping Flasks Looking Great
Notes: Turn valve to sample position while flask is full to empty through valve and wash it out.

## Slide 43: Keeping Flasks Looking Great
Notes: Turn valve to sample position while flask is full to empty through valve and wash it out.

## Slide 44: Organized Inventory
Labeled Parts
  Do You Really Know What’s What?
  How Many “Mystery” Parts Do You Have?
Parts in Compartments/Bins
  Organization = Efficiency
  Efficiency = Speed

## Slide 45: Meter Technician’s Job Responsibilities
  Verification
  Repair and Calibration
  Responsible
For the Very Foundation of the DHI Industry
Be Proud of Your Job and Take Your Responsibilities Seriously

## Slide 46: Resources Available On-Line
QCS website is your source…
  Current auditing guidelines
  List of certified meter centers
  List of certified meter technicians
  List of approved meters and scales
  Links to manufacturers
www.quality-certification.com

## Slide 47: Quality Certification Services Inc.
A simple, yet vital mission….
Providing a reliable source of information to people interested in the U.S. dairy records industry.
Performance & Quality Standards
Compliance Auditing of Providers
Education, Training, & Development